## Slide 1
FY-26: Career Preview Program
Project Review (CPP-3)
Vellore Institute of Technology, Vellore
HPE internal use only
1
Notes: 1

## Slide 2
Project Details
Overview
Project Name:
College
Source Code
HPE Mentor
VIT Mentor
QUIC Traffic Identification, Classification & Policing
Vellore Institute of Technology, Vellore
Sivakumar Ramasamy
Dr. Ruby D
https://github.com/SuvidhJ/QUIC_Identification_and_Policing_HPE_CPP
Project Participants
Kavya Jain
Suvidh Jain
Shubham Kumar
Vansh Chani
Rajan Hasija
HPE internal use only
2

## Slide 3
HPE internal use only
3
Problem Overview
Modern Internet applications are increasingly adopting the QUIC protocol due to its low connection latency, improved reliability, and support for HTTP/3. However, unlike traditional TCP-based protocols, QUIC operates over UDP and encrypts most transport-layer metadata, making it significantly more difficult to identify using conventional packet inspection techniques.
Need for QUIC Classification
Accurate identification of QUIC and Non-QUIC traffic is essential for Internet Service Providers (ISPs), enterprise networks, and network administrators to effectively monitor, manage, and secure network traffic. Since multiple applications with diverse Quality of Service (QoS) requirements use QUIC, simply detecting the protocol is insufficient for efficient traffic management and resource allocation.
Our Objective
To address this challenge, this project proposes a hybrid multi-stage classification framework that first identifies QUIC and Non-QUIC traffic using deterministic rules, memory-assisted lookup, and machine learning. The detected QUIC traffic is then further classified into its application and traffic category to enable application-aware QoS enforcement.
The ubiquity of the QUIC protocol (HTTP/3) has created a visibility crisis for network administrators.
Problem Statement

## Slide 4
HPE internal use only
3
Solution Proposal
We developed an end-to-end, four-stage pipeline to capture, identify, classify, and police encrypted network traffic without relying on standard Deep Packet Inspection (DPI).
MODULE 1: RAW PACKET EXTRACTION
Bypassing standard libraries to manually decode packets at the NIC level (ETH_P_ALL) for real-time, zero-latency performance.
MODULE 2: QUIC IDENTIFICATION
Extracting heuristic evidence (headers) and normalizing 5-tuples to robustly detect QUIC flows via a multi-tier framework.
MODULE 3: QUIC CLASSIFICATION
Training and deploying a SMOTE-balanced XGBoost machine learning model on 14 statistical flow features to categorize traffic.
MODULE 4: QOS POLICING
Applying autonomous, dynamic bandwidth allocation on Open vSwitch (OVS) based on real-time ML traffic inferences.

## Slide 5
HPE internal use only
5
Overall Flow

## Slide 6
HPE internal use only
6
Raw Byte Parsing
Capturing the Packet
We open a raw socket (AF_PACKET) bound to our mirror port (s1-eth3). This gives us every frame that passes through the switch — as raw bytes, straight from the network card. No filtering, no preprocessing. We get the full Ethernet frame exactly as it was sent.
Peeling the Layers
Each packet is wrapped in layers. First we strip the Ethernet header (14 bytes) to get the IP packet. Then we read the IP header to find source/destination IPs and confirm it's UDP. Then we strip the UDP header (8 bytes) to get the payload. What's left is the QUIC data — the part we actually need.
Reading the QUIC Header
From the QUIC payload, we read the first byte to determine if it's a Long or Short header. For Long Headers, we extract the version (4 bytes), then the Connection IDs (DCID and SCID) by reading their length bytes first, then the actual IDs. We also identify the packet type — Initial, Handshake, 0-RTT, or Retry — from bits 4-5 of the first byte.
Instead of relying on heavy third-party libraries (Scapy, aioquic), we manually decode Ethernet, IP, and UDP layers using Python's socket and struct modules.

## Slide 7
HPE internal use only
7
Raw Socket Capture: Captures modified frames using ETH_P_ALL directly from eth0. No OS decoding.
1
L2/L3 Decoding: Manually extracts MACs and EtherType; validates IPv4 and parses IHL for header length. TCP is instantly dropped.
2
QUIC Heuristics: Inspects bits in the UDP payload for Long/Short headers, the Fixed bit (0x40), and extracts Version fields.
3
Flow Normalization: Builds a 5-tuple (sorting IPs/Ports consistently) to track bidirectional flows under a single identity.
4
Manual Decoding Pipeline

## Slide 8
8
QUIC Header Interpretation
Bit-Level Inspection
  Long Header Bit: Most significant bit. Signals handshake establishment, RTT, Version Negotiation, and Retry packets.
  Fixed Bit (0x40): Required by RFC to be 1. Used to distinguish QUIC from other UDP noise.
Heuristic Evidence
If the Long Header is set, we extract the Version Field (4-byte ID) and compare against known variants.
HPE internal use only

## Slide 9
9
Flow Normalization & Evidence
The Normalized 5-Tuple
To ensure bidirectional traffic (Client↔Server) is
recognized as one flow, we sort IP/Port pairs into a consistent order before hashing
Evidence Buffering
Feature extraction begins after the first 5 packets of a normalized bidirectional flow are collected. We aggregate statistics across the window:
  Proportion of packets with Long Header set.
  Diversity of distinct QUIC versions.
  Frequency of specific packet types (Initial, Handshake, 0-RTT).
HPE internal use only

## Slide 10
HPE internal use only
10
Tier 1: Deterministic
Performs rapid deterministic detection utilizing explicit QUIC protocol signatures.
Checks include transport protocol matching, the fixed bit, long header presence, and valid version information verification.
Hybrid Classifier: First, incoming packets are grouped into a 5-packet flow to extract protocol-specific and statistical features. The flow is then processed through a three-tier framework.
Tier 2: Handshake
If Tier 1 is unconfident, the flow proceeds to deeper packet inspection.
The system actively checks for specific QUIC handshake packet types (Initial, Handshake, Retry, 0-RTT, or Version Negotiation).
Tier 3: ML & Lookup
Tier 3a - cached-flow lookup: First performs a memory lookup using previously identified Connection 5-tuples.
Tier 3b - ML fallback: If no match, an ML model classifies the flow using 10 statistical features (Output: QUIC, QUIC_PROBABLE, NON-QUIC).
QUIC Identification

## Slide 11
11
ML Model: Establishing Ground Truth
HPE internal use only
1. Traffic Capture: Used tshark alongside Chrome TLS key logs to capture raw UDP traffic.
2. Decryption & Labeling: Decrypted HTTP/3 headers. Flows were assigned labels (video, audio, web, data) based primarily on content-type, with TLS SNI hostnames as a fallback.
3. Flow Keying: Grouped flows utilizing the QUIC Destination Connection ID (DCID) as the primary key to survive IP migrations.
To train the ML classifier, we built a secure labeling pipeline to capture real-world traffic classes.

## Slide 12
12
Feature Generation
HPE internal use only
Once flows are labeled, the raw traffic is sliced into 5-second time windows (minimum 5 packets). We extract 14 distinct statistical features per window.

## Slide 13
Addressing Data Imbalance
HPE internal use only
Exploratory Data Analysis revealed a massive skew in organic internet traffic, heavily favoring generic Web data.
To prevent the XGBoost model from overwhelmingly biasing towards the majority class, we applied SMOTE (Synthetic Minority Over-sampling Technique).
EDA Observations
13

## Slide 14
14
HPE internal use only
Training & Evaluation
88.6%
Average Cross-validation Accuracy
Average Cross-validationAccuracy
Model Parameters
  300 estimators
  max_depth 6
  learning_rate 0.05.
Feature Importance Insights
The Upload Ratio (0.438) emerged as the single most critical predictor, successfully distinguishing heavily asymmetrical data downloads from symmetrical background web traffic, despite full payload encryption.
0.7886
Average Macro F1

## Slide 15
15
HPE internal use only
Dynamic QoS Policing
Phase 1: Initial State
When the system starts, we create 4 HTB queues on the switch egress port (s1-eth2): Default, Video, Data, and Web. But only the Default queue is active. A catch-all OpenFlow rule (priority 1) sends all traffic to this queue. Since no flows are classified yet, every packet goes through Default and gets equal treatment — first come, first served, full 10 Mbps available.
Phase 2: Flow Gets Classified — OpenFlow Rule Installed
When the ML model predicts a flow's class (say Video), we install a specific OpenFlow rule (priority 100) that matches that flow's 5-tuple (src IP, dst IP, src port, dst port, UDP) and enqueues it into the Video queue (Queue 1). This rule has higher priority than the default, so OVS matches it first. From this point, every packet of that flow goes into the Video queue instead of Default.
Phase 3: Bandwidth Rebalances Automatically
Each queue has a weight — Video: 4, Data: 2, Web: 1, Default: 1. When a new class becomes active for the first time, we recalculate every queue's guaranteed minimum bandwidth using weighted fair share. For example, if only Video and Data are active: Video gets 4/6 of 10 Mbps (~6.6 Mbps min), Data gets 2/6 (~3.3 Mbps min). Default gets whatever is left. Every queue can still burst up to the full 10 Mbps when others are idle. These rates are pushed to the OVS kernel in real time via ovs-vsctl.

## Slide 16
HPE internal use only
DEMO
16

## Slide 17
HPE internal use only
Key Learnings
Raw Sockets Over Libraries
Re-implementing a purpose-built L2-L4 parser via raw Python sockets (ETH_P_ALL) is vastly superior to heavy libraries for achieving zero-latency processing in constrained SDN namespaces.
Understanding QUIC Protocol
Internals
Developed a comprehensive understanding of the QUIC protocol, including Long and Short Headers, Connection IDs, handshake packets, version negotiation, and how QUIC differs from traditional TCP/UDP communication.
ML for Real-World Network
Traffic
Gained practical experience in feature engineering, model training (XGBoost), cross-validation, threshold optimization, SHAP-based interpretability, and evaluating models on unseen network traffic to ensure reliable deployment.
17

## Slide 18
HPE internal use only
18
Conclusion
Major Project Outcomes
  Bypassed the QUIC encryption blindspot using raw byte heuristics and statistical flow modeling.
  Achieved an 88.6% real-time classification accuracy via an optimized, SMOTE-balanced XGBoost architecture.
  Proved the viability of translating ML predictions into autonomous, dynamic QoS policing via Open vSwitch.

## Slide 19
© 2026 Hewlett Packard Enterprise Development LP
Thank You
HPE internal use only
Notes: 6